“Simplified simulations should capture key cell-level behaviors, providing a phenomenological description of cell interactions without requiring prohibitively (ungeheuer) detailed molecular-level simulations of the internal state of each cell. “ [Intro To CC3D -4-]

“Multi-cell simulations are useful to interpolate between single-cell and continuum-tissue extremes because cells provide a natural level of abstraction for simulation of tissues, organs and organisms” [Intro To CC3D -4-]

“The Glazier-Graner-Hogeweg (GGH) approach facilitates (erleichtern) multiscale simulations by defining spatially-extended generalized cells, which can represent clusters of cells, single cells, sub-compartments of single cells… “ [Intro To CC3D -5-]
→ This allows tuning the level of detail in a simulation from intracellular (Occurring or	situated within a cell or cells) to continuum without switching simulation framework

“The effective energy mixes true energies, such as cell-cell adhesion with terms that mimic (nachamen) energies” [Intro To CC3D -6-]

index-copy attempts; change the effective energy, and we accept or reject each attempt

“A Monte Carlo Step consists of one index-copy attempt for each pixel in the cell lattice” [Intro To CC3D -6-]

Fields also evolve due to secretion, absorption, diffusion, reaction and decay according to partial differential equations (PDEs)

Boundary energy; represents variations in energy due to adhesion between cells of different types

CC3D
Python scripts primarily monitor the state of the simulation and implement changes in cell behaviors

Modules which calculate effective energy terms or monitor events on the cell lattice are called plugins

Modules called steppables usally performs operations on cells, not on pixels. Steppables are called at fixed intervals measured in Monte Carlo steps.
Teppables have three main uses:
to adjust cell parameters in response to simulation events
to solve PDEs
to load simulation initial conditions or save simulation results

Great advantage of using Python-only simulations is that parameters appearing in
the configureSim function (this function replaces the CC3DML script) can be Python
variables or Python expressions and this may help users in building simulation codes
which are easit to maintain.

Mitosis = The process in cell division by which the nucleus divides

CC3D refers to each cell type with an number
→ self.MEDIUM, self.CONDENSING, self.NONCONDESING
→ cell.type = self.CONDENSING is equivalent to cell.type=1

pyAttributeAdder, listAdder = CompuCellSetup.attachListToCells (sim)
→ instructs the CompuCell3D kernel to attach a Python-defined list to each cell when it	creates it. This list serves as a generic container which can store any set of Python
objects and hence any set of generalized-cell properties.

PyAttributeAdder, listAdder = CompuCellSetup.attachDictionaryToCells(sim)
→ Attach a pyhton dictionary

Mitosis = Zellteilung (der Kern (die DNA von der Zelle)) wird geteilt
→ das SollVolumen muss auch geteilt werden, da durch dieses die fehler / energie funktion	gesteuert wird

Energiefunktion:
CC3D probiert die Energiefunktion so niedrig wie möglich zu halten. Wir manipulieren den
soll Wert der Funktion, damit die Simulation weiter läuft.
Normalerweise wird nur verkleinert, manchmal wird die Energie / der Fehler aber auch
vergrößert um das globale Maximum zu finden.

Fitnessfunktion = die Abweichung vom echten Gewebe (1 ist perfekt (keine Abweichung))